## Slide 1
AI-Powered Smart Home Assistant
Face Recognition • Voice Control • LLM Integration • Raspberry Pi

## Slide 2
Why This Project?
Goal: Build a hands-on AI + Embedded Systems project combining multiple real-world technologies
  Combines Computer Vision, Speech AI, and Large Language Models in one working system
  Designed for real deployment on edge hardware (Raspberry Pi 4), not just a laptop demo
What it does:
  Recognizes faces at the door and greets people by name
  Registers new/unknown visitors automatically via voice
  Responds to a wake word ("Hey Jarvis") like Alexa/Google Home
  Controls smart home appliances (lights, fans) via natural speech

## Slide 3
High-Level Architecture (Overview)
INPUT LAYER
USB Camera + Microphone
PROCESSING LAYER
OpenCV (Detection) • face_recognition (Identity) • openWakeWord • Speech Recognition
INTELLIGENCE LAYER
Rule-Based Fast Path + Google Gemini API (Function Calling)
OUTPUT LAYER
gTTS (Text-to-Speech) • Hardware Control (Lights / Fans)
DEPLOYMENT TARGET: Raspberry Pi 4 (8GB RAM)

## Slide 4
Detailed Block Diagram — Sensing & Concurrency
USB CAMERA
(Video Frames)
MICROPHONE
(Audio Stream)
PROCESS 1 (independent OS process)
face_recognition_process()
PROCESS 2 (independent OS process)
wake_word_process()
OpenCV DNN: detect_faces_dnn()
Locate face coordinates in frame
read_amplified_chunk()
Adaptive gain - prevents clipping
face_recognition:
Generate 128-d face encoding
openWakeWord model.predict()
Returns confidence score 0.0-1.0
compare_faces() vs
known_faces.pkl database
Score > 0.3 (single hit) OR
> 0.2 twice consecutively?
Known -> Greet (TTS) + log_event()
Unknown -> Voice registration flow
TRIGGERED -> set pause_event
Hand off to run_command_listening()
SHARED MULTIPROCESSING OBJECTS (created once in main(), passed to BOTH processes as arguments)
pause_event (mp.Event) | stop_event (mp.Event) | audio_lock (mp.Lock)
Note: True parallel execution via multiprocessing (separate memory per process) - avoids Python's GIL contention that caused earlier wake-word reliability issues when using threading instead.

## Slide 5
Detailed Block Diagram — Command Processing Logic
Wake word triggered -> run_command_listening()
Google Speech-to-Text API: Audio -> Text Command
Rule-based match?
(try_simple_match)
YES -> Execute Python function directly
(turn_on_light / turn_off_fan / etc.)
Instant - zero API calls
NO -> chat.send_message(command)
Google Gemini API (gemini-3.5-flash)
appliance_state dict checked
(skip action if already ON/OFF)
Gemini analyzes command + available tools list
SDK auto-executes the matching Python function
Gemini formulates final natural-language reply
response_text ready -> returned to main.py's speak()
Note: TESTING_MODE flag in Agent.py mocks Gemini responses during development, preserving the free-tier quota (20 requests/day).

## Slide 6
Detailed Block Diagram — Output & Persistence
response_text received in main.py
speak(response_text, audio_lock)
gTTS: text -> .mp3 file
(requires internet connection)
audio_lock.acquire()
Prevents overlap with other process
playsound: plays .mp3 through speaker -> temp file deleted after
log_event()
-> activity_log.json
(timestamp, event_type, name)
save_database()
-> known_faces.pkl
(only on NEW registration)
pause_event.clear() -> face recognition process resumes
System returns to IDLE / continuous monitoring state
Note: Hardware functions (turn_on_light, etc.) execute IMMEDIATELY when decided - either rule-based or via Gemini function-calling - BEFORE this output stage. Currently simulated via print(); Arduino integration planned next.

## Slide 7
Hybrid AI Architecture (Key Design Decision)
Problem: LLM API calls are slower, cost money, and have rate limits
Solution: Two-tier command processing system
Tier 1 — Rule-Based Matching (instant, free, offline)
  Handles common exact phrases: "turn on light", "turn off fan"
  Zero API calls, millisecond response time
Tier 2 — Gemini LLM with Function Calling (fallback)
  Handles natural/ambiguous language: "it's dark in here"
  AI decides which function to call, executes real actions
Result: Fast AND intelligent, while preserving API quota

## Slide 8
Technology Stack
Computer Vision: OpenCV (DNN detection) • face_recognition / dlib (identity)
Speech: openWakeWord (wake detection) • SpeechRecognition (STT) • gTTS (TTS)
AI / LLM: Google Gemini API • Function Calling / Tool Use
RAG (prototype): sentence-transformers • FAISS vector search
Concurrency: Python multiprocessing (true parallel execution)
Data: pickle (face DB persistence) • JSON (activity logging)
Security: python-dotenv (API key management) • .gitignore practices
Hardware: Raspberry Pi 4 (8GB) • USB Camera • Microphone • Arduino (planned)

## Slide 9
Key Technical Challenges Solved
NumPy 2.x vs OpenCV compatibility conflict -> pinned numpy==1.26.4
Wake-word unreliability -> root cause: GIL contention + USB bandwidth sharing
  Fixed via multiprocessing architecture + separate microphone device
Distance limitation (~3m) -> implemented adaptive audio gain (prevents clipping)
Audio collision race condition -> shared multiprocessing Lock across processes
API quota exhaustion (20/day free tier) -> built mock-testing mode for development
Corporate VPN blocking external services -> identified & documented as constraint

## Slide 10
Engineering Practices Followed
Version control with Git/GitHub — proper commit history throughout development
Secrets management — API keys via .env, never hardcoded or exposed
Graceful degradation — system works even if AI/TTS temporarily unavailable
State management — appliances track ON/OFF state, avoid redundant actions
Alexa-style UX — retry logic for misunderstood commands, timeout handling
Resource-conscious design — frame-skipping, thread limiting for edge deployment

## Slide 11
Current Status
COMPLETE — Face detection & recognition with persistent database
COMPLETE — Voice-based new user registration
COMPLETE — Wake word detection (reliable at 3m+ range)
COMPLETE — Gemini AI agent with function calling
COMPLETE — Hybrid rule-based + LLM command routing
COMPLETE — Multiprocessing architecture for reliability
IN PROGRESS — Arduino integration for physical hardware control
PLANNED — Final deployment & testing on Raspberry Pi 4

## Slide 12
Future Enhancements
Re-activate RAG system for "ask about home history" queries
Offline STT/TTS fallback (Vosk / pyttsx3) for internet-outage resilience
ReSpeaker far-field microphone array for improved range on Pi
Multi-command conversation mode (follow-up questions without re-waking)
Mobile app / web dashboard for remote monitoring

## Slide 13
Thank You
Questions & Discussion